## Slide 1: Financial Payment System Modeling for Polymetallic Nodules
Richard Roth, Randolph Kirchain, Frank Field, Elizabeth Moore Materials System Laboratory Massachusetts Institute of Technology
Presentation to International Seabed Authority Open Ended Working Group on Financial Modeling Kingston, Jamaica March 16, 2023

## Slide 2: Agenda
Quick review of financial payment system options
Review of previous royalty rate results
Updates to the model
  Suggestions from other submissions
  Complexity around Mn
  Sponsor State Tax
  Revised metals prices and costs
Analysis and updated results

## Slide 3: Review of Financial Payment System Options
Goals of Financial Payment System
  ISA receive money in return for transfer of ownership of the nodules
  System needs to be FAIR
  Maximize revenue to the ISA, while still enabling contractors to be economically viable
Notes: Let’s back up – basic things about model

## Slide 4: To Design an Effective System, We Model & Simulate Each Component of the System
Process-based cost models of
  Collector Operations
  Environmental monitoring
  Transport
  Metallurgical processor
Cash Flow Models
  Costs
  Revenues
  Royalties
  Taxes & fees
Compute performance metrics
  Cumulative Payments to the ISA
Image from: Marvasti, A. Env. and Resource Econ (2000) 17: 395.
Nodule Collection
Lift & Platform & Process Water
Transport
Metallurgical Processor
Separate the metals: Co, Cu, Ni, & Mn

## Slide 5: Let’s look at the different types of cash flows throughout the project
Revenues
Expenditures
Prefeasbility & Feasibility
Expenses
Upfront Equipment Investments
Operational Expenditures
Revenues from Sale of Metals
Equipment Salvage Value
Cost of Site Restoration

## Slide 6: Let’s look at the different types of cash flows throughout the project
Revenues
Expenditures
Prefeasbility & Feasibility
Expenses
Upfront Equipment Investments
Net Revenues
Equipment Salvage Value
Cost of Site Restoration
These are the funds to be shared with ISA
Note that revenues will be received by contractors
Royalty payments are the mechanism for sharing those revenues with the ISA

## Slide 7: Let’s look at the different types of cash flows throughout the project
Revenues
Expenditures
Prefeasbility & Feasibility
Expenses
Upfront Equipment Investments
Net Revenues
Equipment Salvage Value
Cost of Site Restoration
What would make a system for revenue sharing FAIR?
What should be the mechanism for calculating the payment to the ISA?
ISA
Contractors

## Slide 8: How can we think about making the payment system FAIR?
Meet revenue targets for ISA/Common Heritage
Within norms of land-based mining payment systems
  The joint report from CRU/RMB laid out some of these norms
  Full MIT report considered these norms when providing values for rates
Neither advantage nor disadvantage seabed mining compared with land-based mining
Sufficient returns to justify upfront investments by contractors
All Proposed System Options can be designed to achieve desired levels of the objectives
The specific quantities of these objectives should be used to set the values of the royalty rates

## Slide 9: Financial Payment Systems Under Consideration
One Stage vs Two Stages:
One stage: same rate in all years
Two stage: rate changes in 2nd stage
Financial Systems:
Fixed ad valorem rate (in each stage)
Variable ad valorem rate (rate changes with metals prices)
Blended ad valorem and profit
Four Options
Fixed ad valorem - one stage
Fixed ad valorem - two stage
Blended Profit – two stage (fixed ad valorem 1st stage, blended profit & fixed ad valorem 2nd stage)
Variable ad valorem - two stage (fixed 1st stage, variable 2nd stage)
All systems can be designed to yield the same revenue to the ISA under baseline conditions

## Slide 10: How to Select a Financial Payment System?
1. Are you willing to sacrifice some early revenue to get a greater total?
3. Willing to implement full accounting system? Willing to accept risks of “gaming” the system?
NO
YES
YES
NO
2. Willing to take on extra downside risk to get more upside rewards?
YES
NO
Option #1
Options #2, 3 or 4
Option #3 (profit based)
Option #4 (variable ad valorem)
Options #1 or 2 (fixed ad valorem)

## Slide 11: Summary & MIT Recommendations for Financial Payment System
One Stage with a Fixed Ad Valorem
Two Stage with a Fixed Ad Valorem
Blended Profit plus Fixed Ad Valorem
Two Stage with a Variable Ad Valorem
Two stage system with a variable ad valorem allows:
ISA to capture a good amount of upside benefits with only limited downside risk.
Can be designed to give higher overall revenues to ISA accepting slightly lower revenues in the 1st stage

## Slide 12: Review of Previous Polymetallic Nodule Royalty Rate Results
Royalty Rate Option | Stage One (first 5 years) | Stage Two (after 5 years)
Option 1 | 4% | 4%
Option 2 | 2% | 6%
Option 3 | 2% | 18.5% (profit tax)
Option 4 |  | 
If Value is less than $850/t | 2% | 5%
If Value is greater than $850/t, but less $925/t | 2% | 6%
If Value is greater than $925/t, but less than $1000/t | 2% | 7%
If Value is greater than $1000/t, but less than $1075/t | 2% | 8%
If Value is greater than $1075/t | 2% | 9%

## Slide 13: Summary of updates to previous results
Suggestions from a variety of other submissions
  Analyzed and addressed previous rates based on submission suggestions
Complexity around Mn
  Chose simpler Mn ore for revenue and costs
Concerns around sponsor state tax
  25% corporate tax rate from sponsor state
  Other rates will be addressed in a second presentation
Updated model with revised metals prices and costs
  Costs inflated to 2022 dollars to match prices

## Slide 14: Key Submissions Since November from Different Stakeholders

## Slide 15: Numerous submissions were made with important and insightful points
Main points from submissions
  Mn basis
  Proposed royalty rates
  Ad valorem vs. profit-based systems
  Sponsored State Tax
  Taxation on transfer of rights
  Concept of fairness
  The model was updated to address and analyze these points.

## Slide 16: The African Submission was particularly detailed with five key issues to address their nine tests
Issue 1: The taxation of the direct and indirect transfer of rights
Issue 2: An additional royalty in lieu of sponsoring state corporate income tax
Issue 3: The valuation of Mn
  Their submission suggested EMM, but they were open to other options as long as the royalties are adjusted accordingly
Issue 4: Fiscal stability
Issue 5: Royalty rates
Based on a number of assumptions and modeling updates, we have addressed these recommendations and have determined a new set of values
Royalty Rate Option | Stage One (first 5 years) | Stage Two (after 5 years) | 
Option 1 | 14.4% | 14.4% | 
Option 2 | 6.4% | 19.3% | 
Option 3 | Hybrid regime: a 5% royalty, 30% profit share and 30% additional profit share | 30% (profit share | 
Option 4 | 6.4% |  | 12/25%

## Slide 17: Nodule Value Determination Issue of Manganese

## Slide 18: Possible Valuation Points
Fully processed metals
  Easy to do for Cobalt, Nickel and Copper
  Challenging for Manganese because there may be multiple final forms of manganese sold
    Electrolytic Manganese Metal (high price, small market)
    Various grades of Ferromanganese (low, medium and high carbon) each with different prices
    Other forms such as silico-manganese
Completely unprocessed nodules
  Currently no transparent, arms length market price exists
  Could derive a nodule transfer price based on metals prices and processing costs
    Some details would need to be worked out
Partially processed nodules
  Value for cobalt, nickel and copper based on metal
  Value for “unprocessed” manganese

## Slide 19: Can we simplify the approach to Manganese?
One approach would be to consider an unprocessed manganese product.
Metallurgical process could be done to only remove the three other metals. The remaining slag, could be sold as a manganese rich product without considering additional processing
Fortunately, this slag is quite similar in composition to currently mined (on land) manganese, and a price index for this product exists
Mn ore prices are typically much lower than those of our refined manganese products
  About $475/t of contained Mn, compared to $1560/t used in model

## Slide 20: Important Criteria for Selecting Valuation Point
Transparency:
  Prices must be full transparent and easy to obtain
Arms Length Transaction
  Prices must represent fair value, not a private one-off deal
Mn Ore Indices
Mn Ore index 37% Mn, FOB Port Elizabeth
Mn Ore index 44% Mn, cif Tianjin
Mn Ore index 46% Mn, Australia
Mn Ore index 38% Mn, 5% Fe, South Africa
Mn Ore index 44-45% Mn, Gabon
Mn Ore index 44-45% Mn, Brazil
Mn Ore index 32% Mn, 20% Fe, South Africa

## Slide 21: Sponsor State Tax Concerns

## Slide 22: How to handle Sponsor State Tax?
25% corporate tax rate from sponsor state
  Net revenues to be shared by contractors & ISA are reduced by this amount
  Effective Tax Rate includes payment of this tax
Concerns that some contractors may not pay any or all of this tax.
  Effective Tax Rate would be much lower than industry standards (40%-50%)
    Is this system still FAIR?
  Contractors have more net revenue that could be shared with ISA
    Are we Maximizing ISA Revenue while allowing contractors to be economically viable?
Other rates will be addressed in a second presentation later in this meeting

## Slide 23: Materials Price Assumptions

## Slide 24: The long-term Manganese price is forecast to be around $4.75/dmtu
38% Mn Ore ($/dmtu) | Year | Reference
4.01 | 2021 | S&P Global
4.50 | 2022 | Statista
4.80 | 2016-2022 | Statista
4.74 | 2018-2021 | S&P Global
4.80 | 2020-2023 | Trading Economics
1. Technavio Analysis: Manganese Mining Market by Application and Geography - Forecast and Analysis 2022-2026
Previous Mn price: $4/dmtu
New Mn price: $4.75/dmtu
Mn Ore Price
USD/mt
7
6.4
5.8
5.2
4.6
3.8
Mn 38% ore price is expected to remain stable1 around the 5-year average of $4.75/dmtu
  38% is representative of the composition of the remaining nodule after removal of Cu, Ni, and Co.
The previous Mn price in the model was $4/dmtu
  Not many forecasts in the literature
  Previous forecast was based on temporary decline of price
Notes: 3.8-6.1

## Slide 25: Despite current low prices, long-term Cobalt is forecast to recover to ~$60,000/t
Chart: Long-Term Forecast
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027
S&P | 65558.7419 | 52155.4665 | 57089.5725 | 56132.2047 | 71171.5921 | 89676.206
Cobalt Blue | 50692 | 58082.8407 | 55782.7602
Previous Co price: $55,000/mt
New Co price: $60,000/mt
Chart: LME Short-Term Forecast
| 44972 | 45061 | 45427
LME | 38000 | 38420 | 39980
Forecast (Real $)
However, various groups believe prices may rise again in the future
Instead of today’s price of $40,000/mt or the highest long-term of $80,000/mt, we assume a Co price of $60,000/mt
Chart: Historical Prices
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | 34081.0142 | 28310.2827 | 62497.0739 | 84193.9634 | 37924.1616 | 34177.7896 | 49965.2432 | 65558.7419
Notes: The Ultimate Guide to the Cobalt Market: 2021 - 2030 - Crux Investor

## Slide 26: In light of Copper prices rising, long-term price raised to $9,000/mt
Chart: Long-Term Forecast
| 2022 | 2023 | 2024 | 2025 | 2027 | 2028 | 2029 | 2030
S&P | 8684.98 | 8222.5903 | 8351.7896 | 8482.4295 | 9522.4174 | 9355.9317 | 8837.0595 | 8750.6665
World Bank | 8700 | 7069.5044
Previous Cu price: $7,000/mt
New Cu price: $9,000/mt
Forecast (Real $)
Copper prices have been rising and current prices around ~$8,900/mt
We assume the long-term price will be $9,000/mt
Chart: LME Short-Term Forecast
| 44972 | 45061 | 45627
LME | 8931 | 8958 | 8900
Chart: Historical Prices
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | 6492.3875 | 5387.9694 | 6778.4557 | 7116.4442 | 6379.6389 | 6347.9929 | 9332.9562 | 8684.98
Notes: CMO-October-2022-forecasts.pdf (worldbank.org)

## Slide 27: Nickel prices has seen a dramatic rise but long-term are expected to revert to $20,000/mt
Chart: Long-Term Forecast
| 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
S&P | 24846.2114 | 22953.5197 | 20972.0751 | 19705.7746 | 18295.6135 | 16831.2275 | 17341.2061 | 16965.6736 | 16190.8994
World Bank | 25000 | 19887.9632
Previous Ni price: $18,336/mt
New Ni price: $20,000/mt
Forecast (Real $)
Nickel prices are rising and futures prices are rising even more
In the long-term, prices are settling below $20,000/mt
Because of the rise, we adjusted the Ni price from ~$18,000/mt to $20,000/mt
Chart: LME Short-Term Forecast
| 44972 | 45061 | 45627
LME | 26900 | 26850 | 28235
Chart: Historical Prices
| 2018 | 2019 | 2020 | 2021 | 2022
 | 14661.3346 | 15170.9467 | 14218.0783 | 18428.0208 | 24846.2114

## Slide 28: Analysis and Results

## Slide 29: Analysis of Royalty Rates with Model Changes
For all four options, the Effective Tax Rate (ETR) served as a basis for selecting rates
  45% was chosen, but other values could be analyzed
Conducted sensitivity analysis around the costs and metals prices
Today, the results focus will be on Option #4
  Two Stage Variable Ad Valorem System

## Slide 30: Under baseline conditions, this system results in a 45.4% ETR 3%  7.5%/12.5%
Stage One (first 5 years)
  Fixed Royalty Rate = 3%
Stage Two (after 5 years)
  If metal value is:
    <$510/t, Royalty Rate = 7.5%
    ≥$510/t, <$580/t, Royalty Rate = 8.75%
    ≥$580/t, <$650/t, Royalty Rate = 10%
    ≥$650/t, <$720/t, Royalty Rate =11.25%
    ≥$720/t, Royalty Rate = 12.5%
The value of the nodule using the new price assumptions is $614/t, resulting in a 10% royalty rate
Effective Tax Rate: 45.4%
ISA lifetime royalty revenue (undiscounted): $5.215 billion
Collector IRR: 17.65%
Notes: 3, 7.5/12.5

## Slide 31: Sensitivity Analysis Results

## Slide 32: If costs are 20% higher than expected, ETR rises to 48.1%
Same system
  3%  7.5/12.5%
Effective Tax Rate: 48.1%
ISA lifetime royalty revenue (undiscounted): $5.215 billion
Collector IRR: 14.07%
 | Baseline CAPEX | 20% Higher CAPEX
Collector | $2.24B | $2.69B
Metals Processor | $1.57B | $1.89B
 | Baseline OPEX | 20% Higher OPEX
Collector | $111/t | $133/t
Metals Processor | $61/t | $73/t

## Slide 33: If costs are 20% lower than expected, ETR falls to 43.3%
Same system
  3%  7.5/12.5%
Effective Tax Rate: 43.3%
ISA lifetime royalty revenue (undiscounted): $5.215 billion
Contractor IRR: 22.06%
 | Baseline CAPEX | 20% Lower CAPEX
Collector | $2.24B | $1.79B
Metals Processor | $1.57B | $1.26B
 | Baseline OPEX | 20% Lower OPEX
Collector | $111/t | $88/t
Metals Processor | $61/t | $49/t

## Slide 34: 20% is a reasonable range for the metals prices sensitivity analysis
 | Today’s Price* | 20% Lower Forecast | Baseline Forecast | 20% Higher Forecast | Typical Range**
Mn Ore | $4.97/dmtu | $3.80/dmtu | $4.75/dmtu | $5.70/dmtu | $3.8-6.1/dmtu
Nickel | $24,815/t | $16,000/t | $20,000/t | $24,000/t | $16,000-28,000/t
Cobalt | $48,874/t | $48,000/t | $60,000/t | $72,000/t | $40,000-80,000/t
Copper | $9,174/t | $7,200/t | $9,000/t | $10,800/t | $6,000-10,000/t
*March 1, 2023 price
**Semi-quantitative assessment of both recent historical and medium-term forecasts.
Range Coverage
Forecast
Today’s
+/-20%
Typical range
Notes: Vertical, horizontal line, represent range
Make box in color +/-20%

## Slide 35: Option 4 is quite effective at dealing with metals price fluctuation
20% higher metals prices
Effective Tax Rate: 47.0%
  ISA lifetime royalty revenue (undiscounted): $7.764 billion
  Contractor IRR: 20.98%
20% lower metals prices
Effective Tax Rate: 44.7%
  ISA lifetime royalty revenue (undiscounted): $3.189 billion
  Contractor IRR: 13.57%
20% lower metals prices

## Slide 36: This system works reasonably well unless both prices and costs fall
  COSTS
  PRICES
0
20%
-20%
-20%
20%
0
45.20%
43.30%
41.80%
47.00%
45.50%
44.70%
49.10%
48.10%
48.80%
Effective Tax Rate (ETR)
Notes: Option 4 is good at addressing the variations in prices

## Slide 37: Option 4 captures price variations
  COSTS
  PRICES
0
20%
-20%
-20%
20%
0
5,737M
4,581M
3,322M
5,132M
3,988M
2,736M
4,556M
3,395M
2,131M
  COSTS
  PRICES
0
20%
-20%
-20%
20%
0
7,764M
5,125M
3,189M
7,764M
5,125M
3,189M
7,764M
5,125M
3,189M
Sponsor State Tax
ISA Revenue
Notes: Option 4 is good at addressing the variations in prices
Does not capture cost variability the way a tax does

## Slide 38: Key Takeaways
This financial payment system is designed to give 45% ETR under baseline assumptions
  Captures upside potential from possible rising metals prices, while minimizing downside potential if prices don’t reach long term forecasts
Model can be re-run to find rates for any assumptions
  E.g., The range of recommended ETR values ranges from 40% to over 50%
  While shown for Option 4, results are available for Options 1-3
System is moderately progressive with regard to metals prices
  Rates change with +/- 20% change in price, but larger increases could also be used
CIT to Sponsor State is assumed to be 25%. A system with an additional rate for those that do not pay 25%, will be shown later